## Slide 1
Chapter 5
Combinational logic circuits
By:Getinet G
Digital Logic Design - ECEG-3161

## Slide 2
4.1 Introduction
4.2 Combination Circuits
4.3 Analysis Procedure
4.4 Design Procedure
4.5 Binary Adder-Subtractor,
4.6 Decimal Adder,
4.7 Binary Multiplier,
4.8 Magnitude Comparator,
4.9 Decoders,
4.10 Encoders,
4.11 Multiplexers ,Demultiplexers
Outline of Chapter 4
1/63

## Slide 3
Logic circuits for digital systems are either:-
  Combinational or
  Sequential
A combinational circuit Contains
  Logic gates and Input variables
  Logic gates :Accept signals from Input & generate signals to output
  outputs at any time are determined from the present combination of inputs only.
Introduction

## Slide 4
Sequential circuits
Employ storage elements(Memory) in addition to logic gates.
Their outputs are a function of inputs and state of the storage elements.
Not only present values of inputs, but also on past inputs.
Circuit behavior must be specified by a time sequence of inputs and internal states.
Introduction

## Slide 5: Combinational Logic Circuits
Output is function of input only
  i.e. No feedback
  When input changes, output may change (after a delay)
•
•
•
•
•
•
n inputs
m outputs
Combinational
Circuits

4/63

## Slide 6: Design Procedure
Given a problem statement:
  Determine the number of inputs and outputs
  Derive the truth table
  Simplify the Boolean expression for each output
  Produce the required logic circuit
Example:
Design a circuit to convert a “BCD” code to “Excess 3” code
4-bits
0-9 values
4-bits
Value+3
?
5/63

## Slide 7: Design Procedure
BCD-to-Excess 3 Converter
A B C D | w x y z
0 0 0 0 | 0 0 1 1
0 0 0 1 | 0 1 0 0
0 0 1 0 | 0 1 0 1
0 0 1 1 | 0 1 1 0
0 1 0 0 | 0 1 1 1
0 1 0 1 | 1 0 0 0
0 1 1 0 | 1 0 0 1
0 1 1 1 | 1 0 1 0
1 0 0 0 | 1 0 1 1
1 0 0 1 | 1 1 0 0
1 0 1 0 | x x x x
1 0 1 1 | x x x x
1 1 0 0 | x x x x
1 1 0 1 | x x x x
1 1 1 0 | x x x x
1 1 1 1 | x x x x
 |  |  |  | C |  |  | 
 |  |  | 1 | 1 | 1 | B | 
A |  | x | x | x | x |  | 
 |  | 1 | 1 | x | x |  | 
 |  |  | D |  |  |  | 
 |  |  |  | C |  |  | 
 |  |  | 1 | 1 | 1 |  | 
 |  | 1 |  |  |  | B | 
A |  | x | x | x | x |  | 
 |  |  | 1 | x | x |  | 
 |  |  | D |  |  |  | 
 |  |  |  | C |  |  | 
 |  | 1 |  | 1 |  |  | 
 |  | 1 |  | 1 |  | B | 
A |  | x | x | x | x |  | 
 |  | 1 |  | x | x |  | 
 |  |  | D |  |  |  | 
 |  |  |  | C |  |  | 
 |  | 1 |  |  | 1 |  | 
 |  | 1 |  |  | 1 | B | 
A |  | x | x | x | x |  | 
 |  | 1 |  | x | x |  | 
 |  |  | D |  |  |  | 
w = A+BC+BD
x = B’C+B’D+BC’D’
y = C’D’+CD
z = D’
6/63

## Slide 8: Design Procedure
BCD-to-Excess 3 Converter
A B C D | w x y z
0 0 0 0 | 0 0 1 1
0 0 0 1 | 0 1 0 0
0 0 1 0 | 0 1 0 1
0 0 1 1 | 0 1 1 0
0 1 0 0 | 0 1 1 1
0 1 0 1 | 1 0 0 0
0 1 1 0 | 1 0 0 1
0 1 1 1 | 1 0 1 0
1 0 0 0 | 1 0 1 1
1 0 0 1 | 1 1 0 0
1 0 1 0 | x x x x
1 0 1 1 | x x x x
1 1 0 0 | x x x x
1 1 0 1 | x x x x
1 1 1 0 | x x x x
1 1 1 1 | x x x x
w = A + B(C+D)
x = B’(C+D) + B(C+D)’
y = (C+D)’ + CD
z = D’
7/63

## Slide 9: 1.Design a Seven-Segment Decoder Group Assignment
a
b
c
g
e
d
f
?
w
x
y
z
a
b
c
d
e
f
g
w x y z | a b c d e f g
0 0 0 0 | 
0 0 0 1 | 
0 0 1 0 | 
0 0 1 1 | 
0 1 0 0 | 
0 1 0 1 | 
0 1 1 0 | 
0 1 1 1 | 
1 0 0 0 | 
1 0 0 1 | 
1 0 1 0 | 
1 0 1 1 | 
1 1 0 0 | 
1 1 0 1 | 
1 1 1 0 | 
1 1 1 1 | 
BCD code
a = ?
b = ?
c = ?
d = ?
8/63
e = ?
g = ?
f = ?
Design the logic circuit

## Slide 10: 2) Design a combinational code converter that converts a 4-bit gray code to binary number. 3)Design a combinational circuit with three inputs, A, B, and C, and three outputs, x, y, and z . When the binary input is 0, 1, 2, or 3, the binary output is one greater than the input. When the binary input is 4, 5, 6, or 7, the binary output is two less than the input.

## Slide 11: Binary Adder
Half Adder
  Adds 1-bit plus 1-bit
  Produces Sum and Carry
HA
x
y
S
C
x y | C S
0 0 | 0 0
0 1 | 0 1
1 0 | 0 1
1 1 | 1 0
x
+ y
───
C S
x
y
S
C
10/63

## Slide 12: Binary Adder
Full Adder
  Adds 1-bit plus 1-bit plus 1-bit
  Produces Sum and Carry
x y z | C S
0 0 0 | 0 0
0 0 1 | 0 1
0 1 0 | 0 1
0 1 1 | 1 0
1 0 0 | 0 1
1 0 1 | 1 0
1 1 0 | 1 0
1 1 1 | 1 1
x
+ y
+ z
───
C S
FA
x
y
z
S
C
 |  |  |  | y | 
 |  | 0 | 1 | 0 | 1
x |  | 1 | 0 | 1 | 0
 |  |  | z |  | 
 |  |  |  | y | 
 |  | 0 | 0 | 1 | 0
x |  | 0 | 1 | 1 | 1
 |  |  | z |  | 
S = xy'z'+x'yz'+x'y'z+xyz = x  y  z
C = xy + xz + yz
11/63

## Slide 13: Binary Adder
Full Adder
x
y
z
S
C
x
y
z
S
C
S = xy'z'+x'yz'+x'y'z+xyz = x  y  z
C = xy + xz + yz
12/63

## Slide 14: Binary Adder
Full Adder
x
y
z
S
C
HA
x
y
z
HA
S
C
13/63

## Slide 15: Binary Adder
c3 c2 c1 .
+ x3 x2 x1 x0
+ y3 y2 y1 y0
────────
Cy S3 S2 S1 S0
FA
x3 x2 x1 x0
FA
FA
FA
y3 y2 y1 y0
S3 S2 S1 S0
C4 C3 C2 C1
0
Binary Adder
x3x2x1x0 y3y2y1y0
S3S2S1S0
C0
Cy
Carry Propagate Addition
14/63

## Slide 16: Parallel Adder : Exercise
  Determine the sum generated by the 3-bit parallel adder below and show the intermediate carries when the binary numbers 101 and 011 are being added.

## Slide 17: Figure 6.9 A 4-bit parallel adder

## Slide 18: Binary Subtractor
Use 2’s complement with binary adder
  x – y = x + (-y) = x + y’ + 1
17/63

## Slide 19: Binary Adder/Subtractor
M: Control Signal (Mode)
  M=0  F = x + y
  M=1  F = x – y
18/63

## Slide 20: Comparators The basic function of a comparator is to compare the magnitudes of two binary quantities to determine the relationships of those quantities.
Compares two n-bit binary values to determine which one is larger.
Inputs : 2 single-bit inputs (X and Y).
Outputs : 3 lines: X>Y, X=Y, X<Y.

## Slide 21: Decoders
Extract “Information” from the code
Binary Decoder
  Example: 2-bit Binary Number
Binary Decoder
x1
x0
Only one lamp will turn on
0
0
1
0
0
0
1
0
2
3
20/63

## Slide 22: Decoders
A decoder has
  N inputs
  2N outputs
A decoder selects one of 2N outputs by decoding the binary value on the N inputs.
The decoder generates all of the minterms of the N input variables.
Exactly one output will be active for each combination of the inputs.
What does “active” mean?

## Slide 23: Decoders
2-to-4 Line Decoder
I1 I0 | Y3 Y2 Y1 Y0
0 0 | 0 0 0 1
0 1 | 0 0 1 0
1 0 | 0 1 0 0
1 1 | 1 0 0 0
Binary Decoder
I1
I0
y3
y2
y1
y0
22/63

## Slide 24: Decoders
“Enable” Control
Binary Decoder
I1
I0
E
Y3
Y2
Y1
Y0
E | I1 I0 | Y3 Y2 Y1 Y0
0 | x x | 0 0 0 0
1 | 0 0 | 0 0 0 1
1 | 0 1 | 0 0 1 0
1 | 1 0 | 0 1 0 0
1 | 1 1 | 1 0 0 0
23/63

## Slide 25: Decoders
3-to-8 Line Decoder
Binary Decoder
I2
I1
I0
Y7
Y6
Y5
Y4 Y3
Y2
Y1
Y0
24/63

## Slide 26: Decoders
Expansion
I2 I1 I0 | Y7 Y6 Y5 Y4 Y3 Y2 Y1 Y0
0 0 0 | 0 0 0 0 0 0 0 1
0 0 1 | 0 0 0 0 0 0 1 0
0 1 0 | 0 0 0 0 0 1 0 0
0 1 1 | 0 0 0 0 1 0 0 0
1 0 0 | 0 0 0 1 0 0 0 0
1 0 1 | 0 0 1 0 0 0 0 0
1 1 0 | 0 1 0 0 0 0 0 0
1 1 1 | 1 0 0 0 0 0 0 0
I2 I1 I0
Binary Decoder
I0
I1
E
Y3
Y2
Y1
Y0
Y7
Y6
Y5
Y4
Y3
Y2
Y1
Y0
Binary Decoder
I0
I1
E
Y3
Y2
Y1
Y0
25/63

## Slide 27: Encoders
An encoder has
  2N inputs
  N outputs
An encoder outputs the binary value of the selected (or active) input.
An encoder performs the inverse operation of a decoder.
Issues
  What if more than one input is active?
  What if no inputs are active?

## Slide 28: Encoders
Put “Information” into code
Binary Encoder
  Example: 4-to-2 Binary Encoder
x3 x2 x1 | y1 y0
0 0 0 | 0 0
0 0 1 | 0 1
0 1 0 | 1 0
1 0 0 | 1 1
1
2
3
Binary Encoder
y1
y0
x1
x2
X3
Only one switch should be activated at a time
27/63

## Slide 29: Encoders
Octal-to-Binary Encoder (8-to-3)
I7 I6 I5 I4 I3 I2 I1 I0 | Y2 Y1 Y0
0 0 0 0 0 0 0 1 | 0 0 0
0 0 0 0 0 0 1 0 | 0 0 1
0 0 0 0 0 1 0 0 | 0 1 0
0 0 0 0 1 0 0 0 | 0 1 1
0 0 0 1 0 0 0 0 | 1 0 0
0 0 1 0 0 0 0 0 | 1 0 1
0 1 0 0 0 0 0 0 | 1 1 0
1 0 0 0 0 0 0 0 | 1 1 1
Binary Encoder
Y2
Y1
Y0
I7
I6
I5
I4 I3
I2
I1
I0
28/63

## Slide 30: Encoder / Decoder Pairs
Y2
Y1
Y0
I7
I6
I5
I4 I3
I2
I1
I0
I2
I1
I0
Y7
Y6
Y5
Y4 Y3
Y2
Y1
Y0
Binary Encoder
Binary Decoder
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0
29/63

## Slide 31: Multiplexers
A multiplexer has
  N control inputs
  2N data inputs
  1 output
A multiplexer routes (or connects) the selected data input to the output.
  The value of the control inputs determines the data input that is selected.

## Slide 32: Multiplexers
Z = A′.I0 + A.I1
Data
inputs
Control
input

## Slide 33: Multiplexers
MUX
Y
I0
I1
I2
I3
S1 S0
S1 S0 | Y
0 0 | I0
0 1 | I1
1 0 | I2
1 1 | I3
32/63

## Slide 34: Multiplexers
2-to-1 MUX
4-to-1 MUX
MUX
Y
I0
I1
S
MUX
Y
I0
I1
I2
I3
S1 S0
33/63

## Slide 35: Implementation Using Multiplexers
MUX
Y
I0
I1
I2
I3
S1 S0
x y | F
0 0 | 1
0 1 | 1
1 0 | 0
1 1 | 1
Example F(x, y) = ∑(0, 1, 3)
x y
F
1
1
0
1
34/63

## Slide 36: Demultiplexers
A demultiplexer has
  N control inputs
  1 data input
  2N outputs
A demultiplexer routes (or connects) the data input to the selected output.
The value of the control inputs determines the output that is selected.
A demultiplexer performs the opposite function of a multiplexer.

## Slide 37: DeMultiplexers
DeMUX
I
Y3
Y2
Y1
Y0
S1 S0
S1 S0 | Y3 | Y2 | Y1 | Y0
0 0 | 0 | 0 | 0 | I
0 1 | 0 | 0 | I | 0
1 0 | 0 | I | 0 | 0
1 1 | I | 0 | 0 | 0
36/63

## Slide 38: Multiplexer / DeMultiplexer Pairs
Y
I7
I6
I5
I4 I3
I2
I1
I0
I
Y7
Y6
Y5
Y4 Y3
Y2
Y1
Y0
MUX
DeMUX
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0
S2 S1 S0
S2 S1 S0
x2 x1 x0
y2 y1 y0
Synchronize
37/63

## Slide 39
Thank You !!!
?